| PART 1 (OPEN TO THE PUBLIC) | ITEM NO. |
| --- | --- |

REPORT OF THE STRATEGIC DIRECTOR OF HOUSING AND PLANNING

TO THE LEAD MEMBER FOR PLANNING

ON 17 JANUARY 2005

TITLE:	PEDESTRIAN FACILITIES - BARTON LANE, ECCLES.

RECOMMENDATIONS:  APPROVAL BE GIVEN TO INSTALL A PUFFIN (PEDESTRIAN

USER FRIENDLY INTELIGENCE) CROSSING ON BARTON LANE BETWEEN OXFORD STREET AND BOARDMAN STREET.

EXECUTIVE SUMMARY: THIS REPORT GIVES DETAILS OF THE PROPOSED PUFFIN

CROSSING ON BARTON LANE AND THE RESULTS OF THE CONSULTATION EXERCISE

WITH WARD COUNCILLORS, RESIDENTS AND EMERGENCY SERVICES.

BACKGROUND DOCUMENTS:  REPORT TO TRAFFIC MANAGEMENT UNIT (19/10/04)

WORKING FILES IN TRAFFIC & TRANSPORTATION SECTION.

ASSESSMENT OF RISK: LOW

THE SOURCE OF FUNDING IS: TRANSPORT CAPITAL PROGRAMME (LOCAL SAFETY SCHEMES 2004/05)

LEGAL ADVICE OBTAINED:	N/A

FINANCIAL ADVICE OBTAINED: N/A

CONTACT OFFICER:	 SEAN FERNANDO

WARD (S) TO WHICH REPORT RELATE (S): ECCLES

KEY COUNCIL POLICIES: ASSISTS IN THE DRIVE TOWARDS CASUALTY

REDUCTION IN SALFORD

DETAILS: The report details the installation of a Puffin Crossing proposal on Barton Lane,Eccles.

- Barton Lane is approximately 1.33 kilometres long, a local distributor that runs between Barton Road and Church Street, Eccles. The junctions at either end and the junction with Corporation Road, which is approximately 150 metres south west of Church Street, are signal controlled. Concerns have been expressed by local residents in the area regarding the level of road safety, particularly about lack of pedestrian facilities, on Barton Lane.

- An analysis of the City Council’s road traffic accident database has shown that there have been 19 reported injury accidents on the section of Barton Lane between Barton Road and Corporation Road, in the three-year study period up to the end of December 2003. Of the 19 accidents 9 were pedestrian/vehicle collisions, which resulted in 11 pedestrian casualties. There have been 4 vehicle/vehicle collisions at the junction of Barton Lane/Trafford Road and the remaining 6 accidents were scattered along the section of Barton Lane between Barton Road and Grand Union Way.

- Speed surveys have recently been carried out at two locations on Barton Lane. The resulting figures showed that the 85th percentile speed (ie the speeds up to which 85% of the vehicles travels in free flow conditions) are in the range from 30mph to 37mph in the vicinity of the proposed Puffin Crossing and 32mph to 40mph in the vicinity of Grand Union Way.

- The road safety problems on Barton Lane can be summarised as lack of pedestrian facilities between Pleasant Road and Talbot Street, vehicle/vehicle collisions at the junction of Barton Lane/Trafford Road and a random distribution of accidents along Barton Lane.

- To address the pedestrian safety problem the City Council is considering the installation of a Puffin (Pedestrian User Friendly Intelligence) Crossing on Barton Lane, approximately 20 metres south west of Oxford Street. The crossing is being proposed at the location where the majority of pedestrian accidents were concentrated and it would give pedestrians a greater sense of protection whilst minimising delays to traffic. Placing of anti-skid surfacing and advanced warning signs on both approaches to the crossing would warn drivers of the need to approach with caution. There are existing waiting restrictions (24 hours) at this location and, therefore, it should not create a detrimental impact on current parking levels. The attached plan no. TT/SF/119/R illustrates the proposed Puffin Crossing layout. A site assessment framework also attached to this report.

- In addition to the above it is intended to place anti-skid surfacing at the junction of Barton Lane/Trafford Road and ‘SLOW’ markings on red background at appropriate locations. Anti-skid surfacing is proposed at the junction of Barton Lane/Trafford Road due to a concentration of vehicle/vehicle collisions, some of which relate to skidding.

- It is anticipated that the above measures will improve safety along Barton Lane and create a safer environment for local residents, particularly for vulnerable road users such as children and elderly people, etc.

- Site observations revealed that pedestrians tend to cross the carriageway during school start/finishing hours at the proposed crossing point as well as at the existing school crossing patrol point, which is approximately 60 metres north. However, the site constraints do not allow locating a Puffin Crossing at the existing school crossing patrol point. Therefore, school crossing patrol operation is to be retained at the current location.

- Initial consultations have been undertaken with Emergency Services, GM Police, GMPTE, and Disabled Persons Association, etc. and there are no objections to the scheme proposals.

- The results of the consultations with local residents are as follows: -

## The number of consultation documents distributed     =  184

## The total number of return slips received                     =   56  (30%)

## The number of slips in favour                                       =   55   (98%)

## The number of slips not in favour                                 =     1   (2%)

As noted above, the majority (98%) of those residents that responded are in favour of the scheme and the one who was not in favour gave no clear reasons.

- The Director of Housing and Planning therefore recommends that the contents of this report be noted and approval be given to install a Puffin Crossing on Barton Lane between Oxford Street and Boardman Street.

##### Estimated Cost

Approximately £50,000 to be funded from Block 3 Transport Capital Program for Local Safety Schemes 2004/5 allocations.

#### Malcolm Sykes

Strategic Director of Housing and Planning