## RAILTRACK/SALFORD BRIDGEGUARD 3 JOINT VENTURE CONTRACT J164

| Br Ref | BRIDGE NAME | BRIDGE TYPE | PROVISION RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | PROVISION FOOTWAY RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | BD 21/97 ASSESSED RATING | SECTION 117 (BE4) ASSESSED RATING REVIEW | SALFORD CITY COUNCIL RESTRICTION RECOMMENDED | AGREED TEMPORARY WEIGHT RESTRICTION TO BE IMPOSED | FURTHER REVIEW BY SALFORD CITY COUNCIL INCLUDING FACTOR OF SAFETY AND THE POTENTIAL FOR INCREASE IN CAPACITY BY ADDITIONAL ANALYSIS | TEMPORARY WEIGHT RESTRICTION TO BE IMPLEMENTED |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | DSE/138 WINDSOR STREET | PRESTRESSED (MAIN SPAN) | NO | - | FOOTWAY EDGE PROTECTION | NO | MAIN & SIDE SPAN CARRIAGEWAY –40 T EDGE BEAM – 0 T FOOTWAY –0 T | MAIN SPAN FAILS BE 4 – EDGE BEAM | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. SALFORD TO UNDERTAKE PRESTRESS INVESTIGATION LONG TERM PLAN REBUILD | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. SALFORD TO UNDERTAKE PRESTRESS INVESTIGATION | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. SALFORD TO UNDERTAKE PRESTRESS INVESTIGATION | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. |
| 2 | DSE/140 WEST EGERTON STREET | ARCH & PRESTRESSED | 7.5 T WITH WIDTH RESTRICTION | YES | WIDTH RESTRICTION | YES | SPAN 1 CARRIAGEWAY –40 T SPAN 2 FAILS DEAD LOAD SPAN 3 CARRIAGEWAY –40 T FOOTWAY –FAILS DEAD | - | NONE | NONE | NONE | NONE |
| 3 | DSE/141 OLDFIELD ROAD (LNWR) | 7 SPANS PLATE GIRDER & JACK ARCH | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | SPAN 1 MAIN BEAM – FE GROUP 1 FOOTWAY – 7.5 T SPAN 2 & 3 MAIN BEAM – 0 T FOOTWAY – FAILS DEAD SPAN 4 MASONRY ARCH - 7.5 T SPAN 5 MASONRY ARCH - 7.5 T FOOTWAY BEAM - 3 T SPAN 6 MASONRY ARCH - 40 T PARAPET BEAM - FAILS DEAD SPAN 7 MAIN BEAM – 40 T FOOTWAY - FAILS DEAD | - | AWAITING SECTION 117 (BE4) ASSESSMENT RATING FROM NETWORK RAIL. ZERO TONNE BRIDGE CLOSURE TO BE CONSIDERED | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | CONFIRMED AS BUS ROUTE AREAS OF WEAKNESS ARE LONGITUDINAL SHEAR AND WEB YIELDING OVER PIER BETWEEN SPAN 2 & 3. LONGITUDINAL SHEAR CAN BE INCREASED TO 7.5 T AND EMERGENCY VEHICLES. WEB YIELDING CAN BE INCREASED TO BETWEEN 3 T AND 7.5 T? FACTOR OF SAFETY ON 40 T IS BETWEEN 1.05 AND 1.21. FURTHER ANALYSIS COULD BE BENEFICIAL. | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |
| 4 | MVE1/14 AGECROFT ROAD | CAST IRON GIRDER | 3 T | YES | NO | - | BRIDGE RECONSTRUCTED. WEIGHT RESRICTION REMOVED. | - | NONE | NONE | NONE | NONE |
| 5 | MVE1/21 RAKE LANE/ PEPPERHILL | PLATE GIRDER JACK ARCH | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | MAIN BEAM- 38 T PARAPET BEAM – 3 T | - | 33 T & FOOTWAY PROTECTION | SUITABLE FOOTWAY EDGE PROTECTION ENSURE GOOD SURFACING | NO FURTHER REVIEW | SUITABLE FOOTWAY EDGE PROTECTION ENSURE GOOD SURFACING |
| 6 | MVE1/5 OLDFIELD ROAD (L & YR) | CAST IRON GIRDER | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | SPAN 1 CARRIAGEWAY – FE GROUP 2 FOOTWAY – FAILS DEAD SPAN 2 CARRIAGEWAY – 0 T FOOTWAY – FAILS DEAD SPAN 3 CARRIAGEWAY – 0 T FOOTWAY – FAILS DEAD SPAN 4 CARRIAGEWAY – 3 T FOOTWAY – 3 T | SPAN 2 PASS BE 4 - 24 T SPAN 3 FAILS BE 4 SPAN 4 FAILS BE 4 | BRIDGE CLOSURE TO BE CONSIDERED AWAITING PROPOSAL FOR RECONSTRUCTION FOR SPANS 3 & 4 BY NETWORK RAIL. POSSIBLE RECONSTRUCTION OF SPANS 1 & 2 BY SALFORD CITY COUNCIL | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | CONFIRMED AS BUS ROUTE CONSIDER NARROWING CARRIAGEWAY TO ELIMINATE KERB BEAMS. 17 T IF KERB BEAMS ARE ELIMINATED. MINIMUM FACTOR OF SAFETY ON 40 T IS 1.13. HOWEVER, BRITTLE NATURE OF CAST IRON NEEDS TO BE HIGHLIGHT AND ALLOWED FOR. | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |
| 7 | MVE1/8 FREDERICK ROAD | WROUGHT IRON PLATE GIRDER | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | MAIN SPAN MAIN BEAMS – FE 1 FOOTWAY - FAILS DEAD SIDE SPAN PARAPET BEAM – 7.5 T FOOTWAY – FAILS DEAD | PASS BE 4 - 24 T | 7.5 T & FOOTWAY PROTECTION SUBJECT TO REANALYSIS | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | CONFIRMED AS BUS ROUTE MINIMUM FACTOR OF SAFETY ON 40 T IS 1.44. | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |
| 8 | MVE1/9 BROUGHTON ROAD | PRESRESSED | NO | - | FOOTWAY EDGE PROTECTION | NO | CARRIAGEWAY –40 T FOOTWAY –3 T | - | FOOTWAY PROTECTION | FOOTWAY PROTECTION | NO FURTHER REVIEW | FOOTWAY PROTECTION |

| Br Ref | BRIDGE NAME | BRIDGE TYPE | PROVISION RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | PROVISION FOOTWAY RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | BD 21/97 ASSESSED RATING | SECTION 117 (BE 4) ASSESSED RATING REVIEW | SALFORD CITY COUNCIL RESTRICTION RECOMMENDED | AGREED TEMPORARY WEIGHT RESTRICTION TO BE IMPOSED | FURTHER REVIEW BY SALFORD CITY COUNCIL INCLUDING FACTOR OF SAFETY AND THE POTENTIAL FOR INCREASE IN CAPACITY BY ADDITIONAL ANALYSIS | TEMPORARY WEIGHT RESTRICTION TO BE IMPLEMENTED |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 9 | WBS1/14 PENDLEBURY TUNNEL | ARCH (SINGLE) | NO | N/A | NO | N/A | 40 T ASSESSMENT LOAD | N/A | NONE | NONE | NONE | NONE |
| 10 | WBS1/15 PENDLEBURY TUNNEL | ARCH (SINGLE) | NO | N/A | NO | N/A | 40 T ASSESSMENT LOAD | N/A | NONE | NONE | NONE | NONE |
| 11 | WBS1/16 BRIDGE STREET | WROUGHT IRON PLATE GIRDER (SINGLE) | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | MAIN BEAM –38T ALL DECK PLATE – 0 T CARRIAGEWAY CROSS BEAM–7.5 T | PASS BE 4 - 24 T (AWAITING DECK PLATE CLARIFICATION) | APPLY TEMPORARY 7.5 TONNE AND FOOTWAY PROTECTION SUBJECT TO REANALYSIS BY SCC (AWAITING DECK PLATE CLARIFICATION) | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | CONFIRMED NOT TO BE A BUS ROUTE. FURTHER ANALYSIS COULD BE BENEFICIAL. MINIMUM FACTOR OF SAFETY ON 40 T IS 1.36. | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |
| 12 | WBS/17 PENDLEBURY ROAD | WROUGHT IRON PLATE GIRDER (SINGLE) | 7.5 T | NO | FOOTWAY EDGE PROTECTION | NO | MAIN BEAM – 40 T PARAPET BEAM – 0 T CARRIAGEWAY DECK PLATE – 0 T CARRIAGEWAY TRANSVERSE BEAM – 38 T | INTERIM PASS | 33 T & FOOTWAY PROTECTION (AWAITING DECK PLATE CLARIFICATION) | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. | NARROWING ADJACENT TO THE BRIDGE. FURTHER ANALYSIS COULD BE BENEFICIAL. | TEMPORARY ROAD NARROWING & FOOTWAY PROTECTION. |
| 13 | WBS/18 STATION ROAD | WROUGHT IRON PLATE GIRDERS (3 SPAN) | 17 T | NO | FOOTWAY EDGE PROTECTION | YES | SPAN 1 MAIN BEAM – 17 T CARRIAGEWAY DECK – 0 T FOOTWAY – 0 T SPAN 2 & 3 MAIN BEAM –40 T CARRIAGEWAY DECK – 0 T FOOTWAY – 0 T | FAILS BE 4 DUE TO CORROSION OF DECK PLATES ON SPAN 2 | 40 T (SALFORD TO REANALYSE TO PROVE BEAMS) (AWAITING DECK PLATE CLARIFICATION) NETWORK RAIL TO REFURBISH DECK PLATES 2005 | 18 T | NETWORK RAIL PROPOSE TO STRENGTHEN BRIDGE IN 2007/8. CORROSION DRIVING STRENGTHENING WORKS. | 18 T |
| 14 | WBS1/26 WARDLEY HALL IND. EST. | WROUGHT IRON PLATE GIRDER (SINGLE) | AWAITING INSTRUCTION FROM NETWORK RAIL | N/A | AWAITING INSTRUCTION FROM NETWORK RAIL | N/A | CARRIAGEWAY - FAILS DEAD FOOTWAY – FAILS DEAD TRANSFER BEAMS – 0 T PARAPET BEAM – FAILS DEAD | - | CLOSURE TO BE CONSIDERED | 40 T WEIGHT LIMIT WITH ONE CENTRAL VEHICLE WIDTH RESTRICTION OPERATED BY TRAFFIC SIGNALS AND FOOTWAY PROTECTION. CALCULATIONS REQUIRED TO CONFIRM | CENTRAL VEHICLE WIDTH ALLOWS 7.5 T ON TRANSVERSE BEAMS. HOWEVER, PARAPET BEAMS STILL FAIL DEAD? MINIMUM FACTOR OF SAFETY ON 40 T IS 1.11. | FURTHER CLARIFICATION REQUIRED FROM NETWORK RAIL. |
| 15 | WBS1/2 FREDERICK STREET | WROUGHT IRON PLATE GIRDER | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | SPAN 1 CARRIAGEWAY –40 T EDGE BEAM – 7.5 T PARAPET BEAM – 40 T DECK PLATE – 0 T FOOTWAY –7.5 T SPAN 2 CARRIAGEWAY –FE GROUP 2 FOOTWAY 7.5 T EDGE BEAM – 7.5 T PARAPET BEAM – 3 T DECK PLATE – 0 T | PASS BE 4 - 24 T (AWAITING DECK PLATE CLARIFICATION | 7.5 T & FOOTWAY PROTECTION (AWAITING DECK PLATE CLARIFICATION) SUBJECT TO REANALYSIS BY SCC | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | CONFIRMED BUS ROUTE. FURTHER ANALYSIS COULD BE BENEFICIAL. MINIMUM FACTOR OF SAFETY ON 40 T IS 1.13. | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |
| 16 | WBS1/4/2 PENDLETON TUNNEL | ARCH (SINGLE) | NO | N/A | NO | N/A | 40 T ASSESSMENT LOAD | N/A | NONE | NONE | NONE | NONE |
| 17 | WBS1/3 GARDNER STREET | WROUGHT IRON PLATE GIRDERS (3 SPAN) | 17 T | NO | FOOTWAY EDGE PROTECTION | NO | SPAN A CARRIAGEWAY –3 T FOOTWAY –3 T SPAN B CARRIAGEWAY –3 T FOOTWAY –7.5 T SPAN C CARRIAGEWAY –3 T FOOTWAY –7.5 T | - | 3 T & FOOTWAY PROTECTION | 3 T WITH LICENSED DISPENSATION FOR GROUP 2FE EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | NO FURTHER REVIEW | 3 T WITH LICENSED DISPENSATION FOR GROUP 2FE EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION |

| Br Ref | BRIDGE NAME | BRIDGE TYPE | PROVISION RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | PROVISION FOOTWAY RESTRICTION REQUESTED BY NETWORK RAIL | APPLIED | BD 21/97 ASSESSED RATING | SECTION 117 (BE 4) ASSESSED RATING REVIEW | SALFORD CITY COUNCIL RESTRICTION RECOMMENDED | AGREED TEMPORARY WEIGHT RESTRICTION TO BE IMPOSED | FURTHER REVIEW BY SALFORD CITY COUNCIL INCLUDING FACTOR OF SAFETY AND THE POTENTIAL FOR INCREASE IN CAPACITY BY ADDITIONAL ANALYSIS | TEMPORARY WEIGHT RESTRICTION TO BE IMPLEMENTED |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 18 | WBS1/23 MOORSIDE ROAD | WROUGHT IRON PLATE GIRDERS (2 SPAN) | NO | - | FOOTWAY EDGE PROTECTION | NO | SPAN 1 MAIN BEAM –40 T PARAPET –25 T CARRIAGEWAY DECK PLATES –0 T FOOTWAY DECK PLATE – FAILS DEAD SPAN 2 MAIN BEAM –40 T PARAPET –40 T CARRIAGEWAY DECK PLATES –0 T FOOTWAY DECK PLATE – FAILS DEAD | PASS (AWAITING DECK PLATE CLARIFICATION) | FOOTWAY (AWAITING DECK PLATE CLARIFICATION) | SUITABLE FOOTWAY EDGE PROTECTION ENSURE GOOD SURFACING EXAMINATION MONITORING OF DECK PLATES | NO FURTHER REVIEW | SUITABLE FOOTWAY EDGE PROTECTION ENSURE GOOD SURFACING EXAMINATION MONITORING OF DECK PLATES |
| 19 | DSE 124 (MONTON RD) OLD WELLINGTON ROAD | WROUGHT IRON PLATE GIRDER (SINGLE) | 17 T | NO | NO | - | LONGITUDINAL –40 T TRANSVERSE –3 T FOOTWAY – 3 T/FE GROUP 2 | PASS BE 4 - 24 T | 40 T WEIGHT LIMIT WITH ONE CENTRAL VEHICLE WIDTH RESTRICTION OPERATED BY TRAFFIC SIGNALS AND FOOTWAY PROTECTION | 40 T WEIGHT LIMIT WITH ONE CENTRAL VEHICLE WIDTH RESTRICTION OPERATED BY TRAFFIC SIGNALS AND FOOTWAY PROTECTION | CONSIDERED NETWORK RAILS ALTERNATIVE PROPOSAL OF 18 T ON TWO LANES WITH SUITABLE FOOTWAY PROTECTION. HOWEVER, INDUSTRIAL ESTATE GOVERNS THE NEED FOR 40 T VEHICLES. | 40 T WEIGHT LIMIT WITH ONE CENTRAL VEHICLE WIDTH RESTRICTION OPERATED BY TRAFFIC SIGNALS AND FOOTWAY PROTECTION |
| 20 | DSE 125 ALBERT ST. | WROUGHT IRON PLATE GIRDER (SINGLE) | 17 T | NO | NETWORK RAIL REQUESTED REAPPRAISAL OF LONGITUDINAL SHEAR | - | MAIN BEAM – 40 T KERB BEAM – 40 T PARAPET BEAM - FAILS DEAD JACK ARCHES – DEAD LOAD ONLY DUE TO INADEQUATE TIE OTHERWISE 40 T | - | 7.5 T & FOOTWAY PROTECTION SUBJECT TO REANALYSIS BY SCC | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION | REVIEW OF THE ASSESSMENT REPORT CONFIRMED THAT THE PREVIOUSLY REPORTED BD 21/97 CAPACITIES WERE INCORRECT. CARRIAGEWAY CAPABLE OF 40 T APART FROM CURRENT INFORMATION SHEET 22 ASSESSMENT OF JACK ARCHES THAT REDUCE CAPACITY TO ZERO T DUE TO INADEQUATE TIES. | FURTHER CLARIFICATION FROM NETWORK RAIL REQUIRED. |
| 21 | DSE 126 (ECCLES STN) CHURCH ST. | BRICK ARCH & PLATE GIRDERS | 17 T | NO | NOT NECESSARY CAR PARK | - | SPAN 1 CARRIAGEWAY –7.5 T (INADEQUATE RESTRAINT –DEAD LOAD ONLY) FOOTWAY –3 T SPAN 2 40 T ASSESSMENT LOAD | PASS BE 4 – 24 T | 7.5 T & FOOTWAY PROTECTION CONSIDER A HEADROOM RESTRICTION | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION CONSIDER A HEADROOM RESTRICTION | NO FURTHER REVIEW | 7.5 T WITH LICENSED DISPENSATION FOR BUSES AND EMERGENCY VEHICLES. SUITABLE FOOTWAY EDGE PROTECTION CONSIDER A HEADROOM RESTRICTION |
| 22 | SCN3 ECCLES NEW ROAD | WROUGHT IRON PLATE GIRDER (SINGLE) | NO | - | NO | - | 40 T ASSESSMENT LOAD | - | NONE | NONE | NONE | NONE |
| 23 | WBS 1/20 CEMETERY RD | WROUGHT IRON PLATE GIRDER (SINGLE) | CURRENT 13 T GVW, 14 T PSV. | YES | FOOTWAY EDGE PROTECTION | NO | MAIN BEAM –40 T KERB BEAM –40T PARAPET –0 T ALL DECK PLATES –0 T | PASS BE 4 – 24 T (AWAITING DECK PLATE CLARIFICATION) | 13 T GVW & 14 T PSV PLUS FOOTWAY PROTECTION (AWAITING DECK PLATE CLARIFICATION) | 13 T GVW & 14 T PSV PLUS FOOTWAY PROTECTION | FURTHER ANALYSIS COULD BE BENEFICIAL. | 13 T GVW & 14 T PSV PLUS FOOTWAY PROTECTION |
| 24 | WBS1/33 OLD CLOUGH LANE | WROUGHT IRON PLATE GIRDER (2 SPAN) | CURRENT 13 T GVW, 14 T PSV. | YES | FOOTWAY EDGE PROTECTION | NO | SOUTH SPAN MAIN - 17 T KERB – 7.5 T PARAPET – 40 T DECK CARR. – 0 T DECK FOOT – FAILS DEAD NORTH SPAN MAIN – GROUP 1 FE KERB – 7.5 T PARAPET –40 T DECK CARR. – 0 T DECK FOOT – FAILS DEAD | 13 T GVW & 14 T PSV PLUS (AWAITING DECK PLATE CLARIFICATION) | 7.5 T & FOOTWAY PROTECTION (AWAITING DECK PLATE CLARIFICATION) SUBJECT TO REANALYSIS BY SCC | 13 T GVW & 14 T PSV PLUS FOOTWAY PROTECTION | NARROWING OF THE CARRIAGEWAY WOULD INCREASE THE CAPACITY | 13 T GVW & 14 T PSV PLUS FOOTWAY PROTECTION |