|  | ITEM NO. |
| --- | --- |

REPORT OF THE STRATEGIC DIRECTOR FOR HOUSING AND PLANNING

TO THE LEAD MEMBER FOR PLANNING

ON 20 JUNE 2005

TITLE :  SPEED MANAGEMENT MEASURES -  GREENLEACH LANE, WORSLEY.

RECOMMENDATIONS :	That Lead Member notes the contents of this report and approves the recommendation.

EXECUTIVE SUMMARY:

The Lead Member approved a Traffic Calming Proposal for Greenleach Lane on 17 January 2005. However, The scheme has been amended following consultation with members of the Boothstown Community Committee.

The purpose of this report is to inform the Lead Member of the revised

scheme proposal, which has been out to consultation with local

residents.

BACKGROUND               The report of the Director for Housing & Planning (17/01/05)

DOCUMENTS :                The report to Traffic Management Unit (24/11/04)

Working files in Traffic & Transportation

ASSESSMENT OF RISK:	            N/A

###### SOURCE OF FUNDING IS:   An estimated cost of  £34,000 to be funded from Block 3 Transport

###### Capital Programme – Local Safety Schemes allocation.

COMMENTS OF THE STRATEGIC DIRECTOR OF CUSTOMER AND SUPPORT SERVICES (or his representative)

1.  LEGAL IMPLICATIONS                                                 Provided by:    N/A

2. FINANCIAL IMPLICATIONS                                           Provided by:    N/A

PROPERTY (if applicable):     N/A

HUMAN RESOURCES  (if applicable)     N/A

CONTACT OFFICER :	            SEAN FERNANDO  -  EXT  3723

WARD(S) TO WHICH REPORT RELATE(S):    WORSLEY

KEY COUNCIL POLICIES:	ENHANCING LIFE IN SALFORD

Reduce the number of people killed or seriously injured on Salford’s roads.

DETAILS (Continued overleaf)

Report

- The City Council’s road traffic accident database has shown that there have been 4 reported injury accidents along Greenleach Lane, which resulted in 7 casualties, in the last three-years.

- The original traffic calming/management scheme that was approved by the Lead Member for Planning included the following: -

## installation of 4 Driver Feedback Signs along Greenleach Lane

## a build-out at Alfred Avenue;

  - anti-skid surfacing at the junctions of Greenleach Lane/Roe Green and Greenleach Lane/Old Clough Lane;

  - ‘Bend ahead’ warning signs and ‘SLOW’ markings on both approaches to the bend in the vicinity of Old Clough Lane;

  - improvements to the existing refuge island at Manthorpe Avenue; and

  - improved road markings and signing as necessary.

The enclosed plan no. TT/SF/178/R illustrates the original scheme layout.

- Although the majority of residents in the Greenleach Lane area were in favour of the scheme, it was referred to Boothstown Community Committee for further consultations, at the request of Members.

- The comments/requests that we received from the members of the Community Committee have been considered and amendments have been made to the original scheme layout. The main amendments to the scheme are as follows: -

  - Deploy only 2 Driver Feedback Signs not 4 as indicated in the original scheme. One in the vicinity of Broad Oak Road and the other in the vicinity of Beesely Green.

  - Introduction of pedestrian facilities, by means of dropped kerbs, at 4 locations on Greenleach Lane where footpaths from the woods lead out on to the carriageway. The possibility of providing central refuge islands at these points has been investigated but it has not been proved feasible, mainly due to the insufficient carriageway width.

  - It is proposed to slow down drivers on either approach to these crossings with the application of 'Rippleprint' patches. This material acts in a similar way to a rumble strip so that vibrations are transmitted inside the vehicle if it is traveling at speed. The beauty of this material is that unlike a rumble strip, very little vibration is transmitted outside the vehicle.

  - Removal of the 'Side road ahead' sign at Manthorpe Avenue for the junction of Alfred Avenue. Erection of a replacement sign along with a 'Road narrows ahead from left' sign for the proposed build-out at Alfred Avenue on a single post at a prominent location in the vicinity of Manthorpe Avenue.

  - The standard colour of the anti-skid surfacing amended to a 'stone' colour, which should be more acceptable for use in conservation area, but will still contrast with the road surface to provide warning at the appropriate locations. Also the application of 'Rippleprint' in 'stone' to suit.

  - Re-align the kerb-radius at Roe Green.

The attached plan no TT/SF/178/R2 illustrates the amended scheme layout.

- The proposed measures should lead to reduced vehicle speeds and create a safer environment for local residents, particularly for vulnerable road users such as children and elderly persons.

Recommendation

- The Strategic Director of Housing and Planning recommends that the contents of this report be noted and approval be given to proceed with the amended scheme, which has been agreed with the members of the Boothstown Community Committee.

#### Malcolm Sykes

Strategic Director of Housing and Planning