| PART 1 (OPEN TO THE PUBLIC) | ITEM NO. |
| --- | --- |

REPORT OF THE STRATEGIC DIRECTOR OF HOUSING & PLANNING

TO THE LEAD MEMBER FOR PLANNING

ON 31st JANUARY 2005

TITLE :	TRAFFIC CALMING PROPOSALS -  LANGWORTHY ROAD AREA.

RECOMMENDATIONS :	APPROVAL BE GIVEN TO ADVERTISE THE TRAFFIC REGULATION ORDERS IN SUPPORT OF TRAFFIC CALMING PROPOSALS FOR THE  LANGWORTHY ROAD AREA.

EXECUTIVE SUMMARY :	THIS REPORT GIVES DETAILS OF TRAFFIC CALMING PROPOSALS IN THE LANGWORTHY ROAD AREA AND THE RESULTS OF THE CONSULTATION EXERCISE WITH WARD COUNCILLORS, RESIDENTS AND EMERGENCY SERVICES.

BACKGROUND DOCUMENTS : REPORT TO TRAFFIC MANAGEMENT UNIT (28/07/04)

WORKING FILES IN TRAFFIC & TRANSPORTATION SECTION.

ASSESSMENT OF RISK:	              LOW

THE SOURCE OF FUNDING IS:	 DEPARTMENT for TRANSPORT GRANT FUNDED.

LEGAL ADVICE OBTAINED:	 N/A

FINANCIAL ADVICE OBTAINED:	 N/A

CONTACT OFFICER :	            PAUL CARTER

WARD(S) TO WHICH REPORT RELATE(S):    LANGWORTHY

KEY COUNCIL POLICIES:	ASSISTS IN THE DRIVE TOWARDS CASUALTY REDUCTION IN SALFORD

DETAILS:	The report details traffic calming proposals for the Langworthy Road area.

- As part of the Neighbourhood Road Safety Initiative traffic calming schemes have been drawn up for areas where it is believed they will reduce the number and severity of accidents involving children. A detailed analysis of  accident records has revealed the Langworthy Road area is one area where such a scheme would be beneficial.

The area under consideration is that bounded by Langworthy Road, Lower Seedley Road, Derby Road and White Street.

- The accident record for the assessment period from 01/06/00 to 31/05/03 reveals the following:-

Number of accidents = 12

Number of casualties = 13

The majority of accidents involve slight injuries with 11 of the 12 falling into this category, the remaining accident resulting in serious injury.

The accidents occurred on and within the boundaries of Langworthy Road, Derby Road, Liverpool Street, White Street & Ashley Street.

A total of 5 out of the 12 accidents involve pedestrians (all 5 involving children) and a further 2 involving cyclists (1 of these involving a child rider). The remaining 5 accidents involve vehicular casualties.

Neither wet road nor dark conditions are of any significance with none occurring in the wet and only 2/12 in the dark.

The ‘grid iron’ pattern of streets in the Langworthy area encourages short cutting along the residential access roads therefore a need to deter ‘rat running’ is required.

- To address this problem it is proposed to introduce the following: -

- 20mph Zone, with 20mph roundels with red zebraflex surfacing together with associated signage to the entrances of the scheme.

## 5 Junction Plateaux, 75mm high kerb to kerb, 1:10 ramps, 6.5m (min) on flat top.

- 31 No. Flat Top Humps, 75mm high, tapered ends, 1:10 ramps, 3.4m long overall.

- 12 No. Round Top Humps, 75mm high, tapered ends, 3.4m long.

- 12 sets of Speed Cushions, 75mm high, 3m long, 1:10 ramps, 1:4 side ramps, width of cushions to be 1.6m with 0.75m central gap.

- 4 sets of Pinch Points, 3m long, build outs to allow a 3.75m gap.

- 2 Chicanes to match existing chicanes on Seedley Park Road.

- Additional Parking Bays on Seedley Park Road, 1.8m wide.

- It is anticipated that these measures will lead to reduced vehicle speeds and create a safer environment for local residents, particularly vulnerable road users such as children and elderly people, etc. The enclosed plan no. TT/PC/NRSI/Lang1 illustrates the scheme layout.

- Consultations have been carried out, with local residents invited to attend drop in sessions held at the Cornerstone Community Centre and also at the Seedley and Langworthy Initiative (SALI) shop on Langworthy Road where they viewed the proposals and commented on the scheme. The overall response to the proposals was extremely positive with the majority of residents in favour of the scheme with requests for additions or alterations to the scheme most of which we were able to accommodate.

- A small number of residents who were not in favour of the scheme gave comments regarding damage to vehicles due to traffic calming. The traffic calming is designed to reduce the speed of cars whilst allowing fire service vehicles, ambulances and buses to travel without hinderance. The features have gradual ramps to prevent damage to vehicles if driven over appropriately, such comments therefore are deemed to be insufficient evidence to prevent the scheme from being implemented.

- The Strategic Director of Housing & Planning recommends that the contents of this report be noted and approval be given to proceed with advertising the required traffic Orders to introduce a 20mph speed limit and traffic calming measures in the Langworthy Road area.

##### Estimated Cost

Approximately £183,000 from Department for Transport grant funding.

#### Malcolm Sykes

###### Strategic Director of Housing & Planning