C)	WARD(S) AFFECTED:		WALKDEN SOUTH

WARD COUNCILLORS:	I D LINDLEY, L TURNER, N TURNER

CONTACT OFFICER:		PAUL CARTER (X4918)

HILTON LANE, WALKDEN – TRAFFIC CALMING SCHEME

As part of the planning conditions for the new Harrop Fold school site and after consultation with residents it has been decided to introduce a 20 mph traffic calmed zone along Hilton Lane from south of Chapelfield Drive to a point adjacent number 406 Hilton Lane.

The 20 mph traffic calmed zone consists of two build outs, one at either end of the zone, two speed tables at the entrance and exit of the new school site and the introduction of speed cushions and flat top road humps. (The existing speed cushions along this stretch will be removed and replaced). In association with these works it is also intended to reconstruct the existing speed cushions that lie outside the proposed zone as these have become un-fit for purpose due to deterioration.

The proposals will reduce the speed of vehicles travelling along Hilton Lane making it safer for the expected number of pedestrians in particular those accessing the new Harrop Fold School.

# 3 Year Accident Analysis

8 personal injury accidents on Hilton Lane

# Estimated Cost

£190,000

Part of the funding is to be provided from the PFI scheme associated with the construction of the school with the remainder of the funding being provided from the Block 3 Budget

# RECOMMENDATION

It is recommended that all the existing traffic calming measures on Hilton Lane be removed and replaced with those shown on the attached drawings and as per the following schedule.

REVOCATION  OF

The City of Salford (Introduction of speed cushions) (Hilton Lane, Walkden, Worsley) Order 2002

INTRODUCTION OF

SPEED CUSHIONS

Hilton Lane – 16 sets

FLAT TOP ROAD HUMPS

Hilton Lane – 3 No

SPEED TABLE

Hilton Lane – 2 No

INTRODUCTION OF

20 MPH SPEED LIMIT

Hilton Lane, south of Chapelfield Drive to a point adjacent to number 406 Hilton Lane