| PART 1 (OPEN TO THE PUBLIC) | ITEM NO. |
| --- | --- |

REPORT OF THE MANAGING DIRECTOR OF URBAN VISION

TO LEAD MEMBER ON 18th April 2005

TITLE :  				Detroit Bridge Refurbishment Scheme

RECOMMENDATIONS : 	That the reduced tender from Bethell Construction Limited be accepted in the sum of £515,808.12 for a reduced scope of work if additional funds are not available.

EXECUTIVE SUMMARY: 	Detroit bridge is an 80m long, 9m wide footbridge spanning Dock 9 at Salford Quays.   The paint system has reached the end of its lifespan and requires renewal.  The existing timber decking is slippery and presents a safety hazard.  It is proposed to replace the timber decking with non-slip Glass Reinforced Plastic (GRP) decking.  Youths are climbing the vertical truss members of the bridge thereby presenting an ongoing safety hazard.  It is proposed to address this problem by installing anti-climb panels.

The total scheme costs based on the tender sums received for the above works exceed the scheme budget.  Negotiations have been held with the Contractor submitting the lowest tender price to bring the total scheme costs within the budget.  This is achievable but requires removing a proportion of the proposed decking works from the contract.  The costs of completing this work as a separate contract at a later date will be significantly greater than if it could be incorporated into the currently proposed contract.

The Contractor must be instructed to commence work as soon as possible in order to enable painting of the superstructure to be completed prior to demobilisation for the Triathlon event in order that the costs remain in accordance with the tendered activity schedule.

BACKGROUND DOCUMENTS :  None

(Available for public inspection)

ASSESSMENT OF RISK:		 The contingency sum will be smaller than normally allowed for on a project of this size.  This will require careful management to ensure the budget is not exceeded.

THE SOURCE OF FUNDING : 	£500,000 has been approved in the 2005/2006 Capital Programme.  An additional £75,000 is sought from Capital Receipts.

LEGAL ADVICE OBTAINED: 	Not Applicable

FINANCIAL ADVICE OBTAINED : D. McAllister

CONTACT OFFICERS : 	Bernard Worthington – x2679

WARD(S) TO WHICH REPORT RELATE(S)  - Ordsall

KEY COUNCIL POLICIES –  Safer Salford

1.0	BACKGROUND

1.1	Detroit Bridge is a steel truss bridge spanning Dock 9 of the Salford Quays and is approximately 80m long by 9m wide.  It was originally used as a railway swing bridge spanning the Manchester Ship Canal to the west of the “Trafford Road Swing Bridge”.  However, with the decline of the docks the railway line became disused and in 1988 the tracks were taken up and the bridge relocated to its present position.  At this time the bridge was refurbished as a footbridge to a design by Arup, which included the complete replacement of the anti-corrosion system, installation of a hardwood timber decking system for pedestrian access only and the addition of a viewing platform suspended beneath the mid-span of the bridge structure.  Detroit Bridge now provides a convenient link for pedestrians between the developments on the north-west side of Dock 9 such as Harbour City, and the Metrolink and those on the south-east side including the The Lowry and The Designer Outlet.

1.2	The timber decking material has become slippery through a combination of dampness and organic growth on its surface.  This has proved hazardous for pedestrians particularly during the colder and wetter months and several accidents have occurred.  Several years ago chicken wire was laid across the deck surface of the main thoroughfare as a temporary means of roughening the surface to provide more grip and prevent further accidents.  In the meantime various possible solutions have been investigated for replacing the timber deck with a safer alternative surface.  Limitations on the permissible deck load to protect the bridge foundations have determined that only a lightweight solution is feasible.  It is therefore proposed that the current timber decking planks be replaced with Glass Reinforced Plastic (GRP) planks.  These GRP planks have a non-slip resin coated/grit surface.

1.3	The bridges anti-corrosion paint system was applied over 15 years ago and is beginning to show signs of having reached the limits of its durability.  Whilst the bridge is generally still in good condition in terms of corrosion, it is proposed to undertake major maintenance of the anti-corrosion system now and to repaint the entire bridge. Because the steel substrate and the current paint system are still in reasonable condition the amount of preparation required to the existing surfaces prior to the application of new paint will be much less extensive and therefore less expensive than if the bridge is allowed to further deteriorate. It will also fully restore the appearance of the bridge.

1.4	The main truss members of the bridge are comprised of riveted lattice girders, which resemble ladders and provide a means of access to the top chord members over 10m above deck level.  Youths have, over a long period of time, been climbing onto the top of the bridge thereby putting themselves and members of the public at significant risk of serious injury.  It is believed that the opportunity must be taken to implement safety measures as part of the refurbishment. It is therefore proposed to install 2.5-3m lengths of flat metal sheeting to the lattice faces of each of the vertical and inclined lattice truss members starting approximately 3m above the deck level.  The aim is to eliminate effortless hand and footholds currently existing over these lengths of the truss members.

  - It has been concluded that the only safe way of carrying out the above works is to close public access to the bridge for the duration of the works.  Whilst Detroit Bridge is not an adopted highway structure it was deemed prudent to apply for an official Temporary Traffic Regulation Order allowing the Contractor to close the bridge whilst they are on site.  A 44 week period has been allowed in the contract commencing at the end of April. This is to take into account several factors:

- The Salford Triathlon is to be held on the 31st July 2005.  The Triathlon course requires competitors to swim in Dock 9 passing under Detroit Bridge. In the past the bridge has proved a significant vantage point for spectators and has figured prominently in international television coverage of the event. It has been instructed that the bridge must be open to the public and devoid of any signs of construction work for the Triathlon event.  As a result the Contractor has been instructed to demobilise completely from site for the Triathlon date and then remobilise after the event.  The impact of this is to be minimised through careful phasing of the works although inevitably there will be an associated cost increase.

- The specified GRP decking product has a long lead in time of approximately 16 weeks.

- It gives the Contractor the flexibility to programme the works in a manner they believe is most advantageous to them submitting a competitive tender.

  - In summary the works involve:

- Replacing existing timber decking to the bridge with GRP decking

- Repainting the entire bridge

- Installing an anti-climb system to all vertical and inclined bridge truss members.

2.0  FINANCIAL DETAILS

2.1	Tender for the works were invited from the following six companies listed below in alphabetical order.

A.E. Yates Limited

Bethell Construction Limited

Galliford Try Construction Limited

Manchester and Cheshire Construction Co. Ltd

T.I. Protective Coatings

Urban Vision Partnership Limited

  - All of the above companies returned tenders that were checked and found to be arithmetically correct.  Of the six Tenders only one, the fourth lowest, was found not to be in full compliance with the tender requirements and therefore deemed invalid.  The Tender sums, excluding any contingency, are listed below in ascending order: -

£535,808.12

£569,200.00

£615,680.00

£668,872.00

£677,158.00

£839,982.15

  - The current budget for the scheme is £575,000 funded from Section 106 (£250,000), and Capital Receipts (£250,000).  A further £75,000 is sought from Capital Receipts.   A  5% contingency must be added to the tender sum to allow for carrying out unforeseen activities that often arise in a scheme of this size. Design and supervision fees must also be obtained from the budget for the project.

| Summary |
| --- |
| Lowest Tender 5% Contingency Fees | £535,808.12 £26,790.40 £40.000 |
| Total | £602,598.52 |
| Budget | £575,000 |
| Predicted overspend | £27,598.52 |

  - In order to bring the project within budget, Bethell Construction Ltd. Were invited to a meeting to discuss possible ways by which their tender price might be reduced.  This meeting took place at the Civic Centre on the 5th April 2005. It was agreed that the ideas discussed would be further considered by Bethel. The following savings were confirmed in writing on 12th April 2005.

Option A

Strip the timber decking from the lower viewing platform and store for re-use on site, paint the viewing platform in accordance with the tender requirements and re-install the existing timber decking (in lieu of GRP ) with a nominal allowance for replacement decking obtained from the main bridge span.

Lump Sum Saving of £20,000

Option B

Delete all painting and re-decking to the lower viewing platform from the contract.

Estimate of saving in excess of £50,000, subject to confirmation by specialist suppliers.

  - Acceptance of either Option A or B will bring the total project costs within the current budget allowing for a minimal contingency sum of £20,000 (4%) in the case of Option  A,  rising to £50,000 (10%) for Option B.  The contract can therefore be awarded with confidence that it can be completed within budget whichever of the two options is adopted.

  - There are however obvious consequences associated with either Option A or B  cost saving measures:

Option A – The problem of the slippery surface of the timber decking will not be eliminated from the lower viewing platform meaning access to this platform will need to remain closed.  The timber decking to this platform may be replaced with GRP decking at any time in the future as a separate contract when further funds become available. Although a relatively simple operation this will invariably be at a much greater cost than the £20,000 required for the works to be incorporated into the present contract.

Option B – Comments are as Option A except that the cost increases of completing these works as a separate contract at a later date will be even more significant due to the access difficulties involved in painting the lower viewing platform in close proximity to water.  It is believed that such a follow on contract with special access and painting requirements may cost as much £150,000.

2.7  	Of the two options discussed it is recommended that Option A be chosen.  The estimated cost of the scheme on this basis is as follows:

Tender			 £535,808.12

Option A Savings	  -£20,000.00

Contingency		    £19,191.88

Fees			   £40,000.00

Total			£ 575,000.00

2.8	The Contractor has stated that in order to comply with the requirements of the triathlon their latest possible start date would be the 2nd May 2005 and they would require 2 weeks advance notice of the start date to plan resources and procure the works.

3.0  CONCLUSION

  - It is proposed to carry out the following works to Detroit Bridge:

- Replace existing timber decking to main deck with GRP planking.

- Repaint the entire bridge.

- Install anti-climb system to all vertical and inclined bridge truss members.

- Replace the timber decking to the lower viewing platform until such time as funding becomes available to replace the timber with GRP.

Two significant safety hazards concerning the slippery timber deck and the ease of with which the bridge can be climbed have been will be removed.

  - All of the tenders received for these works exceed the current budget of £575,000 for the scheme when contingencies and fees are included. However the minimal cost savings agreed with the contractor will bring the total predicted cost within budget.

  - If after contract award further funding can be obtained then the contractor will be instructed to complete the full scheme in order to avoid the negative implications outlined in the report above.

Bill Taylor

Managing Director of Urban Vision